## Slide 2
DESIGN OF A MODULAR, AXIAL-FLUX DIRECT DRIVE PERMANENT MAGNET GENERATOR FOR WIND TURBINES
Aydın BAŞKAYA
January 17, 2018
METU EEE

## Slide 3: Outline
Introduction
Review Of Wind Energy Conversion (WEC) Systems
Design Of The Proposed Axial Flux Generator
Optimization And Design
FEA Verification Of Analytical Design
Conclusions

## Slide 4
Energy crisis in 1970s and environmental problems worked as a catalyst in development progress of wind turbines
Turkish Case(6% - 2015):
83 country, 24 country >1GW worldwide
[6]
Background of Wind Energy Harvesting

## Slide 5
Sizes and power levels of WPPs are increased, hence importance of efficiency and grid connection subjects are also increased.
Grid support
DD generators have larger diameters.
[8]
Market Forecast:

## Slide 6
Gearbox and drivetrain failures are the main reasons of the longest downtimes
Need for regular maintenance, mechanical & thermal losses, reduced efficiency)
Increasing importance of Reliability, Efficiency, Modularity, Fault tolerance, Reduced maintenance costs
[29]
Problem Statement and Research Objective

## Slide 7: Outline
Introduction
Review Of Wind Energy Conversion (WEC) Systems
Design Of The Proposed Axial Flux Generator
Optimization And Design
FEA Verification Of Analytical Design
Conclusions

## Slide 8
Induction Generators
SCIG, WRIG, DFIG
Synchronous Generators
EESG, PMSG-SELECTED TYPE
  (+) Full-scale power converter, variable speed, higher energy yield and efficiency
  (-) Magnet prices, large diameter and mass(DD)
Current Wind Turbine Generator Technologies

## Slide 9
Europe trends on WECs:
[41]
Current Wind Turbine Generator Technologies

## Slide 10: Outline
Introduction
Review Of Wind Energy Conversion (WEC) Systems
Design Of The Proposed Axial Flux Generator
Optimization And Design
FEA Verification Of Analytical Design
Conclusions

## Slide 11
RFPM
  Low torque/volume , long axial length
AFPM SELECTED TYPE
  High torque density, axial length advantage , multistage flexibility
TFPM
  Low power factor, complex structure
[54]
Flux Orientations

## Slide 12
Proposed Generator
Single stage of the selected AFPM generator

## Slide 13
Proposed Generator
Half cross section of C-core
Counter view of one pole
Counter view of winding

## Slide 14
There is a 4/3 ratio between coil pitch and pole pitch in order to get higher induced voltage.
Proposed Generator

## Slide 15
Proposed Generator

## Slide 16
Reluctance network

## Slide 17
Magnet-magnet leakage fluxes are taken into account
Reluctance network

## Slide 18
Flux Density waveform

## Slide 19
50 kW/60 rpm sample verification
 | Analytical | FEA | Error
Peak Airgap Flux Density | 0.67 T | 0.65 T | 3%
Peak Induced Emf Eph,peak | 1496 V | 1600 V | 6.5%

## Slide 20
Structural deflection
Deflection should be below 10% with respect to air gap clearance [71]-[73]
Beam model is used in the calculation of C-Core deflection
Thermal Approach
Forced air cooling selected
Reference current density is used as 7 A/mm2 [50],[79]
8 rotor bars and 6 stator bars[66]

## Slide 21: Outline
Introduction
Review Of Wind Energy Conversion (WEC) Systems
Design Of The Proposed Axial Flux Generator
Optimization And Design
FEA Verification Of Analytical Design
Conclusions

## Slide 22
Genetic Algorithm is selected for the cost-based optimization method.
15 different design parameters of the proposed generator are optimized.
Air gap is selected as constant (10 mm-from 1/1000)[47][82]
Objective function is defined as:
Optimization Characteristics

## Slide 23
Optimization Characteristics
Population Size=100
Number of Generation=200
9 speed intervals with real wind probabalistic
7 different penalty functions

## Slide 24
Koru RES/Çanakkale (52.8 MW) wind speed statistics are processed in MATLAB
Optimization Characteristics

## Slide 25
GAMESA-G128 (5MW) generation curve data is used for targeted generation
Optimization Characteristics
Wind Speed | Average Speed (rpm) | Average Torque (kNm) | Output Power (kW) | Time Probability | Energy Ratio
4 m/s | 1 | 187.5 | 195 | 31,92% | 4,09%
5 m/s | 1 | 4038,5 | 420 | 10,70% | 2,95%
6 m/s | 2.9 | 2606,1 | 786 | 11,26% | 5,81%
7 m/s | 4.8 | 2596,2 | 1296 | 10,12% | 8,61%
8 m/s | 6.7 | 2788,5 | 1943 | 9,07% | 11,57%
9 m/s | 8.6 | 3017,7 | 2699 | 8,37% | 14,84%
10 m/s | 10.5 | 3193,2 | 3487 | 6,30% | 14,43%
11 m/s | 12 | 3344,6 | 4174 | 4,72% | 12,94%
>12 m/s (Rated) | 12 | 4006,4 | 5000 | 7,54% | 24,76%
Weighted Average (time) | 4.7 | 2154,9 | 1522,6 | 100,00% | 100,00%

## Slide 26
Penalty functions are used to convert a constrained problem to an unconstrained problem
Optimization Characteristics
Penalty Function | Constraint | Penalty Coefficient | Coefficient Value
 | Efficiency |  | =5x104 =3x107
 | Deflection |  | 105
 | Axial length |  | 105
 | Outer diameter |  | 108
 | Temperature |  | 105
 | Power |  | =0.1 =1
 | Voltage |  | 106

## Slide 27
Best fitness variation:
Optimized 5MW/12 rpm Generator

## Slide 28
Optimized 5MW/12 rpm Generator
Optimized design parameters (Independent variables):
Parameter | Value
Mean radius- | 4.71 m
Speed | 12 rpm
Number of poles- | 216
Number of parallel stacks- | 6
Outer limb thickness- | 38 mm
Inner limb thickness- | 25.3 mm
Steel web thickness- | 22.4 mm
Number of turns- | 42
Current density- | 2.47 A/mm2
Number of branch- | 6
Height of the winding- | 43 mm
Winding thickness/Coil pitch ratio- | 0.388
Magnet/Steel width ratio- | 0.76
Fill factor- | 0.69
Height of the magnet- | 18.8 mm
Length of the magnet- | 282.7 mm

## Slide 29
Optimized 5MW/12 rpm Generator

## Slide 30
Some of the salient features at rated speed of 12 rpm:
Optimized 5MW/12 rpm Generator
Feature | Value
Mean radius | 4.71 m
Stator outer diameter | 9.9 m
Air gap | 10 mm
Number of poles | 216
Number of turns | 42
Axial length | 1.0 m
Number of axial stack | 6
Voltage per phase (rms) | 371.88 V
Current per phase | 746.9 A
Total copper loss | 206.9 kW
Total eddy loss | 30.1 kW
Net output power | 4992 kW
Efficiency | 95.4%
Phase reactance | 0.111 Ω
Phase resistance | 0.020 Ω
Power factor | 1
Total mass | 119.4 tonne
Material cost | $ 1.30 M
Total cost (including labor) | $ 1.56 M
Total Electricity Generation (annual) | 11.73 GWh
Total Generation Income (annual) | $ 857k

## Slide 31
Optimized 5MW/12 rpm Generator
Chart: 
| Active Steel (tonne) | Copper (tonne) | Magnet (tonne) | Structural Steel (tonne)
 | 18318 | 17126 | 10765 | 72986
Chart: 
| Active Steel | Copper | Magnet | Structural steel
 | 54956 | 171260 | 861231 | 218958

## Slide 32
Performance ratings:
Optimized 5MW/12 rpm Generator
Wind Speed | Rpm | (A/mm2) | (V) | (A) | Desired Power (kW) | Input Power (kW) | Output Power (kW) | Efficiency (%)
4 m/s | 1 | 1.37 | 24.4 | 414.1 | 195 | 244 | 182 | 74.5
5 m/s | 1 | 2.10 | 19.5 | 636.4 | 420 | 372 | 223 | 60.0
6 m/s | 2.9 | 1.69 | 84.3 | 512.0 | 786 | 874 | 777 | 88.8
7 m/s | 4.8 | 1.62 | 146.9 | 489.1 | 1296 | 1385 | 1293 | 93.4
8 m/s | 6.7 | 1.71 | 208.0 | 518.7 | 1943 | 2049 | 1942 | 94.7
9 m/s | 8.6 | 1.85 | 268.7 | 558.3 | 2699 | 2829 | 2700 | 95.4
10 m/s | 10.5 | 1.95 | 329.4 | 588.5 | 3487 | 3639 | 3490 | 95.8
11 m/s | 12 | 2.03 | 377.1 | 615.5 | 4174 | 4346 | 4178 | 96.1
12 m/s | 12 | 2.47 | 371.4 | 746.9 | 5000 | 5230 | 4992 | 95.4

## Slide 33: Outline
Introduction
Review Of Wind Energy Conversion (WEC) Systems
Design Of The Proposed Axial Flux Generator
Optimization And Design
FEA Verification Of Analytical Design
Conclusions

## Slide 34
Air gap flux density verification

## Slide 35
Air gap flux density verification
Property | FEA | Analytical | Error
Air gap flux density - (peak) | 0.474 T | 0.459 (flat-top) T | 3.1%
Air gap flux density fundamental- (peak) | 0.502 T | 0.516 T | 2.7%

## Slide 36
No-load analysis
Property | FEA Value (V) | Analytical Value (V) | Error
Induced emf per-phase rms | 394.5 | 395.6 | 0.27%

## Slide 37
Air cored, low frequency operation, low inductance structure
Phase reactance value do not become dominant in the calculation of phase voltage
Phase voltage verification
Property | FEA Value (V) | Analytical Value (V) | Error
Phase voltage | 365.25 | 371.88 | 1.81%

## Slide 38
Phase voltage verification
Winding | Harmonic No | Frequency (Hz) | Magnitude | % of Fund. Mag.
Winding-2 | 1st (Fundamental) | 21.6 | 547.67 | 100 %
 | 2nd | 43.2 | 1.30 | 0.24 %
 | 3rd | 64.8 | 8.53 | 1.56 %
 | 4th | 86.4 | 0.26 | 0.05 %
 | 5th | 108 | 0.61 | 0.11 %
 | 6th | 129.6 | 0.50 | 0.09 %
 | 7th | 151.2 | 0.71 | 0.13 %
 | 8th | 172.8 | 0.48 | 0.09 %
 | 9th | 194.4 | 0.90 | 0.16 %
 | 10th | 216 | 0.55 | 0.10 %
THD value is calculated as 2% for three windings

## Slide 39
Total eddy loss for one magnet block is calculated as 9.97 W.
Total eddy loss on magnets is 28.8 kW which corresponds to 0.51% of total output power.
Eddy loss coefficient is estimated as 18 kW/m^3.
Eddy loss coefficient estimation

## Slide 40
Model | Type | Power (MW) | Speed (rpm) | Torque (kNm) | Mass (tonne) | Power Density (W/kg) | Torque Density (Nm/kg)
Thesis/Proposed | DD-PMSG | 5 | 12 | 3980 | 119.4 | 41.8 | 33.3
Harokasan | DD-PMSG | 1.5 | 18 | 796 | 47.2 | 31.7 | 16.8
Newgen | DD-PMSG | 4 | 19 | 2011 | 36.4 | 109.8 | 55.2
NREL-AMSC | DD-PMSG | 3.1 | 12.5 | 2370 | 90 | 34.4 | 26.3
Bang et. al. | DD-TFPM | 5 | 12 | 3980 | 90.8 | 55 | 43.8
NTNU Thesis | DD-PMSG | 10 | 13 | 7347 | 260 | 38.4 | 28.2
NREL-AMSC | DD-PMSG | 6 | 12.3 | 4658 | 177 | 33.9 | 26.3
NREL-AMSC | DD-PMSG | 10 | 11.5 | 8305 | 315 | 31.7 | 26.3
Bang et al. | DD-PMSG | 10 | 10 | 9551 | 325 | 30.7 | 29.3
Enercon/E-126-7580 | DD-EESG | 7.58 | 12 | 6035 | 220 | 34.4 | 27.4
The Switch/PMG4250-16 | DD-PMSG | 4.25 | 16 | 2537 | 89 | 47.7 | 28.5
The Switch/PMG3200-12 | DD-PMSG | 3.20 | 12 | 2547 | 80 | 40 | 31.8
The Switch/PMG1650-17 | DD-PMSG | 1.65 | 17 | 926 | 50 | 33 | 18.5
Comparison

## Slide 41
Conclusion
Designed AFPM generator has modularity, reliability, axial length and torque density advantages.
Highy efficiency due to omitted gear-box.
Main disadvantages of the proposed AFPM generator are magnet cost dependency, large diameter and mass.
Air cored structure, hence no core loss and cogging torque exist.
Design optimization is based on cost and considers real wind statistics and generation data.
Structural mass dominates the mass distribution while PM cost dominates the cost distribution.
Analytical design methodology is verified by FEA.